## Slide 1: Contact Tracing with Body-worn IoT Devices
Middleware Technologies for DistributedSystems 2020/2021

## Slide 2: Problem
Keep track of the contacts between devices
If an event of interest happens, inform all the contacts of a given device

## Slide 3: Architecture
Contiki-NG to manage motes
MQTT as communication protocol
Node-RED as back-end manager
Firebase as storage

## Slide 4: Cooja
Project structure:
Event-driven programming pattern
01
Wireless propagation:
Constant Loss Unit-Disk Graph Model (CL-UDGM)
02
Routing:
Routing Protocol for Low-Power and Lossy Networks (RPL)
03
Motes:
Cooja motes
04

## Slide 5: RPL Border-Router
Man-in-the-middle device
Destination-Oriented Directed Acyclic Graph (DODAG) root of the whole network
Allows communication with the internet

## Slide 6: MQTT-UDP Mote
Protothreads to achieve parallel execution (UDP + MQTT)
MQTT as Finite-State-Machine
Publish-Subscribe pattern
Different topics for different communications

## Slide 7: UDP Signaler
Device used to trigger events of interest
Multicasts a special message to all motes in its range
Triggers the publish of a special message used by the back-end

## Slide 8: Database
NoSQL realtime database
First level dedicated to each node
Second level dedicated to all the contacts of that node

## Slide 9: Node-RED – Contacts Flow
Read the /contatcts/# topic
If the contact isn’t already in the Database, a pair it’s added in the contacts list of both members
Multi level wildcard (#) to receive messages from all motes
MQTT QoS set at 1

## Slide 10: Node-RED – Signal Flow
Read the /signals/# topic
Pull from the DB all the contacts of a given address
Publish a notification message on each contact
Dump the list of contacts
Multi level wildcard (#) to receive messages from all motes
MQTT QoS set at 1

## Slide 11: Testing & Conclusion
After some time the tree topology is created
Motes communicate and print «Publishing Complete»
Motes close to the purple one will signal the event of interest